# LOCAL HIGHWAY AUTHORITY CONSULTATION

To: Cherwell District Council

| Planning Application No | 11/01180/REM | Planning Officer | Linda Griffiths |
| --- | --- | --- | --- |
| OCC ref No | n/a | OCC Officer | n/a |
| Date | 16/09/11 | Comments | Conditions |

Location: Land South West Of Bicester Adjoining Oxford Road & Middleton Stoney Road, Bicester

Oxfordshire

Description: Reserve Matters (ref. Outline 06/00967/OUT) - Access Road to serve the commercial zone within the SW Bicester development site.

Comments

The proposed access 150m road (cul-du-sac) is to be 7m in width with 1.5m grass verges and 2m footways on either side – such dimensions are acceptable due to the expected HGV traffic that is expected to use this commercial route.

The material to be used was to be of a permeable nature, however with the type of vehicles expected to use this route the Local Highway Authority have agreed to revert back to a tarmac surface i.e. permeable material will fail with constant HGV traffic movements.

The proposed drainage arrangements have been confirmed acceptable in principle by the Drainage Engineer; subject to the constructions details and design being submitted to secure written approval from the LPA and LHA prior to work commencing on this access road - this can be conditioned.

Taking the above into account the Local Highway Authority has no objections subject to:

- That before the proposed are first occupied, the whole of the estate roads and footpaths (except for the final surfacing thereof) shall be laid out, constructed, lit and drained and if required temporary or permanent traffic calming to the Oxfordshire County Council’s Specifications.

- Prior to the commencement of work on the Commercial Access Road the construction design and details are to be submitted and approved in writing by the Local Planning Authority.  Such works shall be constructed strictly in accordance with the highway authority’s specifications and that all ancillary works specified shall be undertaken.

- Development to be in accordance with existing Construction Travel Plan.

Signed: M.Deadman

For Oxfordshire County Council as Local Highway Authority

Officer Name: Michael Deadman

Officer Title: Principal Engineer