| Cherwell District Council Planning & Development Services Bodicote House White Post Road Bodicote Banbury OX15 4AA | Our ref: WA/2013/115328/01-L01 Your ref: 13/01056/OUT Date: 08 August 2013 |
| --- | --- |

# Dear Ms Wright,

OUTLINE - UP TO 200 RESIDENTIAL UNITS, ACCESS, AMENITY SPACE AND ASSOCIATED WORKS

SOUTH LODGE FRINGFORD ROAD CAVERSFIELD BICESTER OX27 8TH

Thank you for consulting us on this matter. We received the letter on 12 July 2013 and we are now in a position to respond.

Environment Agency position

In the absence of an acceptable Flood Risk Assessment (FRA) we object to the grant of planning permission and recommend refusal on this basis for the following reasons:

- The applicant has not demonstrated that the storage volume required to attenuate surface water run-off from the critical 1 in 100 chance in any year storm event, with an appropriate allowance for climate change, can be provided on site.

- The applicant has not demonstrated that the peak discharge rate for all events up to and including the 1 in 100 chance in any year critical storm event, including an appropriate allowance for climate change, will not exceed that of the existing site.

- The applicant has not demonstrated that infiltration to dispose of all surface water from the site is achievable through the techniques proposed, especially in view of the ground conditions and groundwater level.

This may increase the flood risk on site and in surrounding areas.

Overcoming our objection

The applicant must demonstrate through their surface water strategy that the proposed development will not create an increased risk of flooding from surface water. Surface water for up to the 1 in 100 chance in any year storm event, including an allowance for climate change, must be safely contained on site. It may be acceptable for limited flooding to occur in parts of the site during this event, ensuring that buildings are not affected by flooding and the site can be safely navigated by users. Where this flooding will be within roads or pathways, the applicants must ensure that safe access and egress is still available.
 
The applicant should complete Section 5.9 of the Flood Risk Assessment which appears to be incomplete.
 
The value of QBar of 2.6 l/s calculated for the existing permeable area seems very low. The applicant should check that this has been correctly derived and check that it has been converted to l/s and pro-rata’d for sites <50Ha.
 
The applicant should clarify that the estimated peak runoff rate from the proposed site includes an appropriate allowance for climate change.
 
The applicant should provide calculation sheets to verify the storage volume, peak discharge rate and infiltration elements of the FRA.
 
The surface water strategy should be carried out in accordance with the National Planning Policy Framework and PPS25 Practice Guide giving preference to infiltration over discharge to a watercourse, which in turn is preferable to discharge to surface water sewer.
 
Advice to LPA/Applicant

Guidance on the preparation of surface water strategies can be found in the Defra/Environment Agency publication "Preliminary rainfall runoff management for developments". Guidance on climate change allowances can be found within the National Planning Policy Framework Technical Guidance.
 
The applicant should, as part of the surface water strategy, demonstrate that the requirements of any local surface water drainage planning policies have been met and the recommendations of the relevant Strategic Flood Risk Assessment and Surface Water Management Plan have been considered.
 
The CIRIA publication ‘C635 Designing for exceedance in urban drainage - Good practice’ contains advice on surface water conveyance and storage. The document can be accessed at www.ciria.com/suds/ciria_publications.htm
 
Surface water run-off should be controlled as near to its source as possible through a sustainable drainage approach to surface water management (SUDS). SUDS are an approach to managing surface water run-off which seeks to mimic natural drainage systems and retain water on or near the site as opposed to traditional drainage approaches which involve piping water off site as quickly as possible. SUDS involve a range of techniques including soakaways, infiltration trenches, permeable pavements, grassed swales, ponds and wetlands. SUDS offer significant advantages over conventional piped drainage systems in reducing flood risk by attenuating the rate and quantity of surface water run-off from a site, promoting groundwater recharge, and improving water quality and amenity.
 
The variety of SUDS techniques available means that virtually any development should be able to include a scheme based around these principles.
 
Further information on SUDS can be found in:

- PPS25 Practice Guide

- CIRIA C522 document Sustainable Drainage Systems – design manual for England and Wales

- CIRIA C697 document SUDS manual

# Yours sincerely,

Mr Jack Moeran

Planning Advisor

# Direct dial 01491 828367

Direct e-mail planning-wallingford@environment-agency.gov.uk

cc Cerda Planning Ltd