LAP Design Guidance

A lap is required for every housing development of 10 or more dwellings.  It provides a play facility for toddlers and children aged up to 6 years.

The number of LAP’s required will depend on site layout but should be within 1 minutes’ walking time of home or approximately 100m along measured footways.  LAP’s should be overlooked by nearby houses.

All LAP’s should contain the following:

- Fencing 1000mm high around the perimeter. Bow top.

- Two gated entry/exit points, gates should be self closing and open outwards to facilitate a quick escape and prevent dogs entering.

- The footpath must extend up to safety surfaces around items of equipment to allow wheelchair and all weather access

- A bench which should be located on hard standing and should have a back and arm rests and be located at least 1m from the boundary fence.

- Hard surfaces to be wheelchair accessible - no loose gravel or stone.

- A playground sign is required. The easiest way to procure this is for the developer to make a contribution payable to Cherwell District Council which we will pass on to the adopter of the playground.

- Play equipment and/or play features to a unique design

- They should have a buffer zone 5m deep between the edge of the activity area and nearest part of any dwelling facing the LAP.  The buffer zone should contain planting to allow children to experience scent, colour and texture.  The planting should be low level to allow surveillance

- A ‘No Dogs’ sign to be located in the ground at each entrance.

- A bin with a locking top is required. Sited 3m from the seat.

- Items of play equipment should be linked to the entrance path with hard surfacing.

- Timber edgings to surfaces should not be used as they are not durable enough

- Areas of pre-cast concrete slabs should not be used, due to maintenance issues.

- Loose materials are to be avoided due to the possibility of them being thrown around

- Wet pour is the preferred safety surface as it is easy to clean.

- Avoid siting metal slides facing south to avoid overheating of the slide surface.

- At least 3 pieces of equipment should be provided. One should provide opportunities for multiple activities.

- The developer is to provide a temporary sign with his contact details on for the period that he is maintaining the play area

- The play area is to be locked until Practical completion is achieved

Revised 11/5/2011