# FIGURE 6.12 - PREDICTED TEMPORARY LANDSCAPE IMPACTS

| LANDSCAPE RECEPTORS | LANDSCAPE VALUE | PROPOSAL | IMPACTS | IMPACT MAGNITUDE | IMPACT SIGNIFICANCE | MITIGATION | RESIDUAL IMPACT SIGNIFICANCE |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Langford Brook | Moderate (Local) | Retention of grassland paddocks and associated vegetation of areas adjacent to Langford Brook. Construction of residential properties/local facilities/school within 40m of the river corridor. Associated haulage routes, construction compounds, fixed and mobile plant, excavations, soil stripping and removal of vegetation. | Potential change in the setting of the Langford Brook through visual disturbance as a result of construction activity. | Low | Negligible-Low | Ensure protective fencing is erected in accordance with BS 5837 to protect any retained important vegetation. Protective hoardings and construction setback zones will also ensure that the watercourse is not contaminated or disrupted. | Low Beneficial |
| Public Footpaths ref. 3 & ref. 4 | County | Construction of residential properties/local facilities/school within 1m of public footpaths. Associated haulage routes, construction compounds, fixed and mobile plant, excavations, flood alleviation works, soil stripping and removal of vegetation. | Potential change in the setting of the footpath through reduced quality and changed character of setting, as a result of construction activity in close proximity and as a result of temporary closure. | Medium | Medium | Clear signage to alert uses of temporary proposed footpath diversion. Protective fencing erected to ensure site security and safety. Large sections of the existing footpath will be separated by protective fencing from the development works to maintain and control access and prevent potential hazards. Temporary diversions away from construction traffic and activity will be required at various stages in the construction process. | Medium Adverse |
| Field Boundary Hedgerows | Moderate (Local) | Construction of residential properties/local facilities/school within 5m of field boundaries. Associated haulage routes, construction compounds, fixed and mobile plant, excavations, flood alleviation works, soil stripping and removal of vegetation. | Clearance of limited sections of tree belts / field boundary hedgerows (approximately 593m). Presence of construction activity and haulage routes. Potential damage to existing hedgerows and ditches to be retained. | Medium | Low | Ensure protective fencing is erected in accordance with BS 5837 to protect any retained important hedgerows. | Low Adverse |
| Individual trees | High (Local) | Construction of residential properties/local facilities/school within 15m of individual trees. Associated haulage routes, construction compounds, fixed and mobile plant, excavations, flood alleviation works, soil stripping and removal of vegetation. | Clearance of a limited number of trees (6no. in total). Presence of construction activity and haulage routes. | Low | Low | Ensure protective fencing is erected in accordance with BS 5837 to protect any retained important trees. | Low Adverse |
| Pasture Fields and Riverside Meadows | High (Local) | Construction of residential properties/local facilities/school within 1m of public footpaths. Associated haulage routes, construction compounds, fixed and mobile plant, excavations, soil stripping and removal of vegetation. | Clearance of areas of existing pasture associated with the development area. Presence of construction activity and haulage routes. | Medium | Low-Medium | Width of construction area minimised in order to retain larger areas of grassland. | Low Adverse |