# From: Judith Ward 
Sent: 15 December 2014 10:13
To: Caroline Ford
Subject: 14/01832/REM Longford Park Marina adj Canal Lane Bodicote

Hi Caroline

This drawing does not have sufficient information on it. I would be very surprised if a Marina wouldn’t have facilities for elsan disposal and a water supply at the very minimum.

If there is an area for boat manoevering presumably there is a slipway?

Is there to be an office or boat repairers?

There is no life belt indicated or separation of the car parking from the marina. There needs to be some sort of barrier to prevent small children running over to the water directly.

It isn’t clear what the surface materials are.

There is no indication that the levels work. There is a fall of 0.5m over the basin site. How does the grading work? Where is the cut and fill going? Need to see proposed contours. Also cross sections through the site.

The turning  angle into the car park looks very tight to me. We need to see proof that it is possible to get a low loader and boat in.

Has advice been sought from a suitably qualified engineer?

Have these proposals been run past the Rivers and Canals Trust (formerly British Waterways) for advice ?

The proposal needs to be developed in far more detail.

Judith

Judith Ward

Landscape Planning Officer

Environmental Services

Cherwell and South Northants Councils’

Direct dial 01295 221711 Extension 1711

Mailto:judith.ward@cherwellandsouthnorthants.gov.uk