Arboricultural Comments (Development applications):

Date:				01809/2015

Comments by:	C. Morrey (Arboricultural Officer – North)

Comments to:			Caroline Ford

CDC Reference:		15/00839/REM

Site Address:	Longford Park Parcel D and E Phase 5

Longford Park Road

Bodicote

Applicant / Agent (highlight one):	Bovis Homes Ltd

Applicants name/address (if different):

Statutory Protection:			 None

T.E.M.P.O guidance notes completed:	 Yes / No

Date of site visit:	Desktop Assessment

Trees / Proposal (brief description):	Reserved Matters to 05/01337/OUT - 125 residential units on Parcels D and E

Significant comments:	The trees identified on site are all category C trees apart from one horse chestnut classified as category U.  As many of the C category trees should be retained as possible to ensure some continuity of tree cover.  The tree protection plan produced is not very clear.  It is difficult to read.  I am happy with the tree species to be planted.  There should a mix of tree sizes planted with some 14-16 sized standard trees.  It looks as though some of the trees may be planted in hard landscaped areas.  If this is the case then we will need to see the tree pit design for these areas.  All tree pits within 3 metres of a hard surface should be lined with root barrier to stop the tree roots from disturbing the adjacent hard surface.  These should be marked on a map.  I am happy with the tree pit design for soft landscaped areas.

Recommendations:	Submit a clearer tree protection plan.  Ensure that there is a mix of tree sizes to be planted to include some 14-16 sized trees.  All tree pits within 3m of a hard surface should be lined with root barriers.  Submit a tree pit design for hard landscaped areas which should incorporate silva cells or equivalent in the planting pit to provide sufficient soil volume for the successful establishment of the trees being planted.